## Slide 1: Introduction
ECC 702 Mobile Communication
Venkataramanan V
EXTC Department
D.J. Sanghvi College of Engineering, Mumbai.

## Slide 2: Course Details
Staff: V.Venkataramanan
Email : venkataramanan.v@djsce.ac.in
rvvenkat.mtech@gmail.com

## Slide 3: Recommended Textbooks
1. Theodore S. Rappaport , ―Wireless Communications, Prentice Hall of India, PTR publication
2. Andreas Molisch , ―Wireless Communications, Wiley, Student second Edition.

## Slide 4: Recommended Textbooks
3. Vijay Garg , ―Wireless Network Evolution 2G-3G, Pearson Education.
4. Young Kyun Kim and Ramjee Prasad, ―4 G Roadmap and Emerging Communication Technologies ―, Artech house.:

## Slide 5: Recommended Textbooks
5. Raj Pandya , ―Mobile And Personal Communications Systems And Services, Prentice hall.
6. Singhal , ―Wireless Communication, TMH
7. C.Y Lee , ―Mobile Communication, Wiley
8. Upena Dalal ―Wireless and Mobile Communications, Oxford university Press.

## Slide 6: Outline
Introduction
  The concept of Mobile radio propagation, cellular system design.
  To understand mobile technologies like GSM and CDMA
  To know the mobile communication evolution of 2G, 3G and 3 GPP in detail
  To have overview of Emerging technologies for 4 G standards.

## Slide 7: Outline
Fundamentals of Mobile Communication

## Slide 8: Outline
Mobile Radio Propagation

## Slide 9: Outline
2G Technologies

## Slide 10: Outline
3G Technology

## Slide 11: Outline
3 GPP LTE

## Slide 12: Outline
Advanced techniques for 4G deployment

## Slide 13: What is Wireless and Mobile Communication?

## Slide 14: Wireless Communication
Transmitting voice and data using electromagnetic waves in open space
Electromagnetic waves
    Travel at speed of light (c = 3x108 m/s)
    Has a frequency (f) and wavelength (l)
        c = f x l
    Higher frequency means higher energy photons
    The higher the energy photon the more penetrating is the radiation

## Slide 15: Electromagnetic Spectrum
104
102
100
10-2
10-4
10-6
10-8
10-10
10-12
10-14
10-16
104
106
108
1010
1012
1014
1016
1018
1020
1022
1024
IR
UV
X-Rays
Cosmic
Rays
Radio
Spectrum
1MHz ==100m 100MHz ==1m
10GHz ==1cm
< 30 KHz VLF 30-300KHz LF
300KHz – 3MHz MF 3 MHz – 30MHz HF 30MHz – 300MHz VHF
300 MHz – 3GHz UHF
3-30GHz SHF
> 30 GHz EHF
Micro wave
Visible light

## Slide 16: Wavelength of Some Technologies
GSM Phones:
  frequency ~= 900 Mhz
  wavelength ~= 33cm
PCS Phones
  frequency ~= 1.8 Ghz
  wavelength ~= 17.5 cm
Bluetooth:
  frequency ~= 2.4Gz
  wavelength ~= 12.5cm

## Slide 17: Frequency Carries/Channels
  The information from sender to receiver is carrier over a well defined frequency band.
    This is called a channel
  Each channel has a fixed frequency bandwidth (in KHz) and Capacity (bit-rate)
  Different frequency bands (channels) can be used to transmit information in parallel and independently.

## Slide 18: Simplex Communication
Normally, on a channel, a station can transmit only in one way.
    This is called simplex transmision
To enable two-way communication (called full-duplex communication)
    We can use Frequency Division Multiplexing
    We can use Time Division Multiplexing

## Slide 19: Duplex Communication - FDD
FDD: Frequency Division Duplex
Base Station
B
Mobile Terminal
M
Forward Channel
Reverse Channel
Forward Channel and Reverse Channel use different frequency
bands

## Slide 20: Duplex Communication - TDD
TDD: Time Division Duplex
A singe frequency channel is used. The channel is divided into time slots. Mobile station and base station transmits on the time slots alternately.
Time division duplex (TDD) refers to duplex communication links where uplink is separated from downlink by the allocation of different time slots in the same frequency band. It is a transmission scheme that allows asymmetric flow for uplink and downlink data transmission.
Base Station
B
Mobile Terminal
M
M
B
M
B
M
B

## Slide 21: What is Mobility
Initially Internet and Telephone Networks is designed assuming the user terminals are static
    No change of location during a call/connection
    A user terminals accesses the network always from a fixed location
Mobility and portability
  Portability means changing point of attachment to the network offline
  Mobility means changing point of attachment to the network online

## Slide 22: Degrees of Mobility
Walking Users
    Low speed
    Small roaming area
    Usually uses high-bandwith/low-latency access
Vehicles
    High speeds
    Large roaming area
    Usually uses low-bandwidth/high-latency access
    Uses sophisticated terminal equipment (cell phones)

## Slide 23: The Need for Wireless/Mobile Networking
Demand for Ubiquitous Computing
  Anywhere, anytime computing and communication
    You don’t have to go to the lab to check your email
  Pushing the computers more into background
    Focus on the task and life, not on the computer
    Use computers seamlessly to help you and to make your life more easier.
  Computers should be location aware
    Adapt to the current location, discover services

## Slide 24: Some Example Applications of Ubiquitous Computing
You walk into your office and your computer automatically authenticates you through your active badge and logs you into the Unix system
You go to a foreign building and your PDA automatically discovers the closest public printer where you can print your schedule and give to your friend

## Slide 25: How to realize Ubiquitous Computing
Small and different size computing and communication devices
  Tabs, pads, boards
  PDAs, Handhelds, Laptops, Cell-phones
A communication network to support this
  Anywhere, anytime access
  Seamless, wireless and mobile access
  Need for Personal Communication Services (PCS)
Ubiquitous Applications
  New software

## Slide 26: Wireless System Definitions
  Mobile Station
      A station in the cellular radio service intended for use while in motion at unspecified locations. They can be either hand-held personal units (portables) or installed on vehicles (mobiles)
  Base station
      A fixed station in a mobile radio system used for radio communication with the mobile stations. Base stations are located at the center or edge of a coverage region. They consists of radio channels and transmitter and receiver antennas mounted on top of a tower.

## Slide 27: Wireless System Definitions
  Mobile Switching Center
      Switching center which coordinates the routing of calls in a large service area. In a cellular radio system, the MSC connections the cellular base stations and the mobiles to the PSTN (telephone network). It is also called Mobile Telephone Switching Office (MTSO)
  Subscriber
      A user who pays subscription charges for using a mobile communication system
  Transceiver
      A device capable of simultaneously transmitting and receiving radio signals

## Slide 28: Wireless System Definitions
  Control Channel
      Radio channel used for transmission of call setup, call request, call initiation and other beacon and control purposes.
  Forward Channel
      Radio channel used for transmission of information from the base station to the mobile
  Reverse Channel
      Radio channel used for transmission of information from mobile to base station

## Slide 29: Wireless System Definitions
  Simplex Systems
      Communication systems which provide only one-way communication
  Half Duplex Systems
      Communication Systems which allow two-way communication by using the same radio channel for both transmission and reception. At any given time, the user can either transmit or receive information.
  Full Duplex Systems
      Communication systems which allow simultaneous two-way communication. Transmission and reception is typically on two different channels (FDD).

## Slide 30: Wireless System Definitions
  Handoff
      The process of transferring a mobile station from one channel or base station to an other.
  Roamer
      A mobile station which operates in a service area (market) other than that from which service has been subscribed.
  Page
      A brief message which is broadcast over the entire service area, usually in simulcast fashion by many base stations at the same time.

## Slide 31: Cordless Telephones
Cordless
Phone
Base unit
PSTN
Telephone
Network

## Slide 32: Cordless Telephones
Characterized by
  Low mobility (in terms of range and speed)
  Low power consumption
  Two-way tetherless (wireless) voice communication
  High circuit quality
  Low cost equipment, small form factor and long talk-time
  No handoffs between base units
Appeared as analog devices
Digital devices appeared later with CT2, DECT standards in Europe and ISM band technologies in USA

## Slide 33: Cordless Telephones
Usage
  At homes
  At public places where cordless phone base units are available
Design Choices
  Few users per MHz
  Few users per base unit
    Many base units are connected to only one handset
  Large number of base units per usage area
  Short transmission range

## Slide 34: Cordless Phone
Some more features
  32 Kb/s adaptive differential pulse code modulation (ADPCM) digital speech encoding
  Tx power <= 10 mW
  Low-complexity radio signal processing
      No forward error correction (FEC) or whatsoever.
  Low transmission delay < 50ms
  Simple Frequency Shift Modulation (FSK)
  Time Division Duplex (TDD)

## Slide 35: Cellular Telephony
Characterized by
  High mobility provision
  Wide-range
  Two-way tetherless voice communication
  Handoff and roaming support
  Integrated with sophisticated public switched telephone network (PSTN)
  High transmit power requires at the handsets (~2W)

## Slide 36: Cellular Telephony - Architecture

## Slide 37: Cellular Telephony Systems
Mobile users and handsets
  Very complex circuitry and design
Base stations
  Provides gateway functionality between wireless and wireline links
  ~1 million dollar
Mobile switching centers
  Connect cellular system to the terrestrial telephone network

## Slide 38: Paging Systems
One-way communication (SX)
Send short message to mobile unit (pager)
Wide area coverage
Page broadcast from many base stations simultaneously to remote units
no information as to user location
Reliable communication everywhere (need good Signal to Noise performance)

## Slide 39: Paging Systems
Requires large Tx power and low data rate
(~ 2-8 kbps)
Noise has less of an effect when the data rate is lower.
Coverage needed even inside buildings w/ 20-30 dB signal attenuation
Needs an extensive network of transmitters to transmit the signal everywhere

## Slide 40: Paging Systems

## Slide 41: Cellular Phone Call Timing
Mobile Identification Number (MIN) is the subscriber's telephone number
Electronic Serial Number (ESN) is device identifier.
Station Class Mark (SCM) identifies the class of the device, based on its maximum transmit power level.

## Slide 42: How a Cellular Telephone Call is Made

## Slide 43: How a Cellular Telephone Call is Made

## Slide 44: Comparison of Common Mobile Radio Systems

## Slide 45: Comparison of Common Mobile Radio Systems

## Slide 46: Cellular Networks
First Generation
    Analog Systems
    Analog Modulation, mostly FM
    AMPS
    Voice Traffic
    FDMA/FDD multiple access
Second Generation (2G)
    Digital Systems
    Digital Modulation
    Voice Traffic
    TDMA/FDD and CDMA/FDD multiple access
2.5G
    Digital Systems
    Voice + Low-datarate Data
Third Generation
    Digital
    Voice + High-datarate Data
    Multimedia Transmission also

## Slide 47: 2G and Data
2G is developed for voice communications
You can send data over 2G channels by using modem
Provides adat rates in the order of ~14.4 Kbps
Increased data rates are requires for internet application
This requires evolution towards new systems: 2.5 G

## Slide 48: 2.5 Technologies
Evolution of TDMA Systems
  HSCSD for 2.5G GSM
      Up to 57.6 Kbps data-rate
  GPRS for GSM and IS-136
      Up to 171.2 Kbps data-rate
  EDGE for 2.5G GSM and IS-136
      Up to 384 Kbps data-rate
Evolution of CDMA Systems
  IS-95B
      Up to 64 Kbps

## Slide 49: 3G Systems
Goals
  Voice and Data Transmission
    Simultanous voice and data access
  Multi-megabit Internet access
    Interactive web sessions
  Voice-activated calls
  Multimedia Content
    Live music

## Slide 50: 3G Systems
Evolution of Systems
    CDMA sysystem evaolved to CDMA2000
        CDMA2000-1xRTT: Upto 307 Kbps
        CDMA2000-1xEV:
        CDMA2000-1xEVDO: upto 2.4 Mbps
        CDMA2000-1xEVDV: 144 Kbps datarate
    GSM, IS-136 and PDC evolved to W-CDMA (Wideband CDMA) (also called UMTS)
        Up to 2.048 Mbps data-rates
        Future systems 8Mbps
        Expected to be fully deployed by 2010-2015
    New spectrum is allocated for these technologies

## Slide 51: Upgrade Paths for 2G Technologies
IS-136 PDC
GSM
IS-95
IS-95B
HSCSD
GPRS
EDGE
W-CDMA
EDGE
TD-SCDMA
cdma200-1xRTT
cdma2000-1xEV,DV,DO
cdma200-3xRTT
2G
2.5G
3G

## Slide 52: GSM and CDMA Coverage Map Worldwide

## Slide 53: Multiple Access
Narrowband Systems
Narrowband systems support low-bit-rate transmission;
Systems operating with channels substantially narrower than the coherence bandwidth are known as narrowband system;
In narrowband systems, all the components of signals are equally influenced by multipath propagation;
Narrowband systems are affected by selective fading.

## Slide 54: Multiple Access
Wideband Systems
wideband systems support high-bit-rate transmission;
Wideband systems operate with channels substantially wider than the coherence bandwidth;
In wideband systems, the various frequency components of the signal may be differently affected by fading.

## Slide 55: Multiple Access
Wireless networks are multiuser systems in which information is conveyed by means of radio waves.
In a multiuser environment, access coordination can be accomplished via several mechanisms:
by insulating the various signals sharing the same access medium;

## Slide 56: Multiple Access
by allowing the signals to contend for the access;
or by combining these two approaches.
The choice for the appropriate scheme must take into account a number of factors, such as:
type of traffic under consideration;
available technology;
cost and complexity

## Slide 57: Multiple Access
Access coordination may be carried out in different domains:
frequency domain
time domain
code domain
space domain.
Four main multiple access technologies are used by the wireless networks:
frequency division multiple access (FDMA)
time division multiple access (TDMA)
code division multiple access (CDMA)
space division multiple access (SDMA).

## Slide 58: Multiple Access

## Slide 59: Multiple Access (International Cocktail Party)
FDMA – Large room divided up into small rooms. Each pair of people takes turns speaking.
TDMA – Large room divided up into small rooms. Three pairs of people per room, however, each pair gets 20 seconds to speak.
CDMA – No small rooms. Everyone is speaking in different languages. If voice volume is minimized, the number of people is maximized.

## Slide 60: General Specification of TDMA
Rx: 869-894MHz Tx: 824-849MHz
832 Channels spaced 30kHz apart (3 users/channel)
DQPSK modulation scheme
48.6kbps bit rate
Interim Standard (IS) – 54
Digital AMPS (Advanced Mobile Phone System)
Uses Time Division Duplexing (TDD) usually

## Slide 61: TDMA Operation
Efficiency of TDMA frame:

## Slide 62: Advantages of TDMA
Flexible bit rate
No frequency guard band required
No need for precise narrowband filters
Easy for mobile or base stations to initiate and execute hands off
Extended battery life
TDMA installations offer savings in base station equipment, space and maintenance
The most cost-effective technology for upgrading a current analog system to digital

## Slide 63: Disadvantages to using TDMA
Requires network-wide timing synchronization
Requires signal processing fro matched filtering and correlation detection
Demands high peak power on uplink in transient mode
Multipath distortion

## Slide 64: TDMA Frame Structure
Preamble | Information message | Trail Bits
Slot 1 | Slot 2 |  | Slot N
Trail Bit | Sync Bit | Information Bit | Guard Bits

## Slide 65: FDMA Operation
Number of FDMA Channels
In the U.S. each cellular carrier is allocated 416 channels where:

## Slide 66: General Specification of FDMA
Rx: 869-894MHz Tx: 824-849MHz
832 Channels spaced 30kHz apart (3 users/channel)
DQPSK modulation scheme
48.6kbps bit rate
Used in analog cellular phone systems (i.e. AMPS)
Uses Frequency Division Duplexing (FDD)
ISI (Inter symbol Interference) is low

## Slide 67: Advantages of FDMA
If channel is not in use, it sits idle
Channel bandwidth is relatively narrow (30kHz)
Simple algorithmically, and from a hardware standpoint
Fairly efficient when the number of stations is small and the traffic is uniformly constant
Capacity increase can be obtained by reducing the information bit rate and using efficient digital code
No need for network timing
No restriction regarding the type of baseband or type of modulation

## Slide 68: Interference
Co Channel Interference: Crosstalk from two different radio transmitters using the same frequency.
Adjacent-channel interference : Interference caused by extraneous power from a signal in an adjacent channel.
Inter symbol Interference : Reflected Signal with Smaller Amplitudes

## Slide 69: Disadvantages to using FDMA
The presence of guard bands
Requires right RF filtering to minimize adjacent channel interference
Maximum bit rate per channel is fixed
Small inhibiting flexibility in bit rate capability
Does not differ significantly from analog system

## Slide 70: General Specification of CDMA
Rx: 869-894MHz Tx: 824-849MHz
20 Channels spaced 1250kHz apart (798 users/channel)
QPSK/(Offset) OQPSK modulation scheme
1.2288Mbps bit rate
IS-95 standard
Operates at both 800 and 1900 MHz frequency bands

## Slide 71: CDMA Operation
Spread Spectrum Multiple Access Technologies

## Slide 72: Advantages of CDMA
Many users of CDMA use the same frequency, TDD or FDD may be used
Multipath fading may be substantially reduced because of large signal bandwidth
No absolute limit on the number of users
Easy addition of more users
Impossible for hackers to decipher the code sent
Better signal quality
No sense of handoff when changing cells

## Slide 73: Disadvantages to using CDMA
As the number of users increases, the overall quality of service decreases
Self-jamming
Near- Far- problem arises (The near-far problem is a condition in which a receiver captures a strong signal and thereby makes it impossible for the receiver to detect a weaker signal.)

## Slide 74: Hybrid Spread Spectrum Techniques
Hybrid combinations that provide certain advantages.
Hybrid FDMA CDMA (FCDMA) — This technique can be used as an alternative to the DS-CDMA techniques
The available wideband spectrum is divided into a number of sub spectras with smaller bandwidths.
Each of these smaller sub channels becomes a narrowband CDMA system having processing gain lower than the original CDMA system.

## Slide 75: Hybrid Spread Spectrum Techniques
The required bandwidth need not be continuous and different users can be allotted different sub spectrum bandwidths.
The capacity of this FDMA/CDMA technique is calculated as the sum of the capacities of a system operating in the sub spectra.

## Slide 76: Hybrid Direct Sequence / Frequency Hopped Multiple Access
Direct sequence modulated signal whose center frequency is made to hop periodically in a pseudorandom fashion

## Slide 77: Hybrid Direct Sequence / Frequency Hopped Multiple Access
Direct sequence, frequency hopped systems - advantage - avoid the near-far effect.
However, frequency hopped CDMA systems are not adaptable to the soft handoff process. [Soft handoff refers to the overlapping of repeater coverage zones]
It is difficult to synchronize the frequency hopped base station receiver to the multiple hopped signals.

## Slide 78: Time Division CDMA (TCDMA)
In a TCDMA (also called TDMA/ CDMA) system, different spreading codes are assigned to different cells.
Within each cell, only one user per cell is allotted a particular time slot.
At any time, only one CDMA user is transmitting in each cell.
When a handoff takes place, the spreading code of the user is changed to that of the new cell.

## Slide 79: Time Division Frequency Hopping (TDFH)
This multiple access technique has an advantage in severe multipath or when severe co-channel interference occurs.
The subscriber can hop to a new frequency at the start of a new TDMA frame, thus avoiding a severe fade or erasure event on a particular channel.
This technique has been adopted for the GSM standard.
Hop : Move by jumping on one foot

## Slide 80: Time Division Frequency Hopping (TDFH)
This scheme also avoids co-channel interference problems between neighboring cells
Two interfering base station transmitters are made to transmit on different frequencies at different times.
The use of TDFH can increase the capacity

## Slide 81: Space Division Multiple Access (SDMA)
Space division multiple access (SDMA) controls the radiated energy for each user in space.
Sectorized antennas may be thought of as a primitive application of SDMA
A sector antenna is a type of directional microwave antenna with a sector-shaped radiation pattern.
Adaptive antennas used to simultaneously steer energy in the direction of many users

## Slide 82: Space Division Multiple Access (SDMA)
Transmit power is limited by battery Consumption at the subscriber unit.
Adaptive antennas used at the base station promise to mitigate some of the problems on the reverse link.
The perfect adaptive antenna system is not feasible since it requires infinitely large antennas

## Slide 83: Frequency Reuse
Cell
R
(a) Ideal cell
(b) Actual cell
R
R
R
R
(c) Different cell models

## Slide 84: Choosing the Shape of a Cell
without overlap and with equal area, there are three sensible choices: a square; an equilateral triangle; and a hexagon.
A cell must be designed to serve the weakest mobiles within the footprint, and these are typically located at the edge of the cell.
The hexagon has the largest area of the three.
the hexagon closely approximates a circular radiation pattern which would occur for an Omni-directional base station antenna and free space propagation.

## Slide 85: Frequency Reuse
consider a cellular system which has a total of S duplex channels available for use
If each cell is allocated a group of k channels
If the S channels are divided among N cells
the total number of available radio channels can be expressed as S=kN

## Slide 86: Frequency Reuse
The N cells which collectively use the complete set of available frequencies is called a cluster.
If a cluster is replicated M times within the system, the total number of duplex channels, C, can be used as a measure of capacity and is given
C = MkN = MS

## Slide 87: Signal Strength
Select cell i on left of boundary
Select cell j on right of boundary
Ideal boundary
Cell i
Cell j
-60
-70
-80
-90
-100
-60
-70
-80
-90
-100
Signal strength (in dB)

## Slide 88: Signal Strength
Signal strength contours indicating actual cell tiling. This happens because of terrain, presence of obstacles and signal attenuation in the atmosphere.
-100
-90
-80
-70
-60
-60
-70
-80
-90
-100
Signal strength (in dB)
Cell i
Cell j

## Slide 89: Handoff Region
BSi
Signal strength due to BSj
E
X1
Signal strength due to BSi
BSj
X3
X4
X2
X5
Xth
MS
Pmin
Pi(x)
Pj(x)
By looking at the variation of signal strength from either base station it is possible to decide on the optimum area where handoff can take place.

## Slide 90: Cell Structure
F2
F3
F1
F3
F2
F1
F3
F2
F4
F1
F1
F2
F3
F4
F5
F6
F7
(a) Line Structure
(b) Plan Structure
Note: Fx is set of frequency, i.e., frequency group.

## Slide 91: Frequency Reuse Structure
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F1
F1
F1
Fx: Set of frequency
7 cell reuse cluster
Reuse distance D

## Slide 92: Reuse Distance
F1
F2
F3
F4
F5
F6
F7
F1
F2
F3
F4
F5
F6
F7
F1
F1
Reuse distance D
For hexagonal cells, the reuse distance is given by
R
where R is cell radius and N is the reuse pattern (the cluster size or the number of cells per cluster).
Reuse factor is
Cluster

## Slide 93: Reuse Distance Contd
The cluster size or the number of cells per cluster is given by
where i and j are integers.
N = 1, 3, 4, 7, 9, 12, 13, 16, 19, 21, 28, …, etc.
The popular value of N being 4 and 7.
i
j
60o

## Slide 94: Reuse Distance Contd
(b) Formation of a cluster for N = 7 with i=2 and j=1
60°
1 2 3 … i
j direction
i direction
(a) Finding the center of an adjacent cluster using integers i and j (direction of i and j can be interchanged).
i=2
i=2
j=1
j=1
j=1
j=1
j=1
j=1
i=2
i=2
i=2
i=2

## Slide 95: Reuse Distance Contd
(c) A cluster with N =12 with i=2 and j=2
j=2
j=2
j=2
j=2
j=2
j=2
i=2
i=2
i=2
i=2
i=2
i=2

## Slide 96: Frequency Reuse
Frequency Reuse is the core concept of cellular mobile radio
Users in different geographical areas (in different cells)
may simultaneously use the same frequency channel
Frequency reuse drastically increases user capacity and
spectrum efficiency
Frequency reuse causes mutual interference
(trade off between link quality and subscriber capacity)

## Slide 97: Frequency Reuse
Cluster:
set of different frequencies used in group of cells
Cluster is repeated by linear shift
i
steps along one direction
j
steps in the other direction
Honeycomb (hexagonal) cell structure

## Slide 98: Frequency Reuse
Distance between cell centers
=
× Cell Radius
Reuse distance
distance between the centers of two co-channel cells
u
2
2
R
=
i
+
j
+
2ij
3
3
R
cos
p
where
R
is Cell Radius
R
u
is Reuse Distance
and
cos(
p
/3) = 1/2
3

## Slide 99: Frequency Reuse
Radius of a cluster
c
u
2
2
R
=
R
3
=
i
+
j
+
ij
3
R

## Slide 100: Frequency Reuse
We have seen
u
R
=
R
3C
and also
u
2
2
R
=
i
+
j
+
ij
3
R
Thus:
C
=
i
+
j
+
ij
2
2
with integer
i
and
j
.

## Slide 101: Handoff Strategies
“When a mobile moves into a different cell while a conversation is in progress, MSC transfers the call to a new channel belonging to the new base station”. (Hard handoff)
In modern wireless systems, there may be no change in the actual channel; only the base station changes (Soft Hand off).
Mobile Switching Center needs to:
Identify the new base station
Allocate new Voice and Control channels associated with the new base station.

## Slide 102
Desired Behavior:
  Prioritize Hand off to new call initiation
  Successful transfer of call
  Hand off should be as infrequent as possible
  Hand off should be imperceptible (very slight)
Hand off Threshold Power Level:
  There is a minimum power level of the signal at BS for acceptable voice quality. (-90 to –100 dBm).
  Hand off Threshold is defined D dBm above this level, so that the system has time to process hand off.
102

## Slide 103: Margin D needs to be neither too small, nor too large
D too small  too short time to perform handoff, The call may be dropped in the meanwhile.
D too large  unnecessary handoff burden. Hand off becomes more frequent, and occurs even when Power is at the acceptable level.
Call will be dropped if
  D is too small,
  Delay in MSC processing because of:
High Traffic hours, New channel not available

## Slide 104: Handoff Basics

## Slide 105: When to Hand off? MSC needs to ensure
When to Hand off? MSC needs to ensure:
  that the power drop is not temporary: because of FADING.
  that MS is actually moving away from the current BS.
MSC measures signal strength for some time (average received signal power). These calculations are performed to:
  Avoid the unnecessary hand off,
  Complete the necessary hand off before call drops
The time available to decide hand off depends on the subscriber’s speed.
Speed of the user can be estimated from the slope of the short term average Power. Steep curve Quick Hand off

## Slide 106: First Generation Systems
Signal Strength Measurements are made by base stations and supervised by MSC.
Each base station constantly monitors power levels of its reverse voice channels, which tells the relative location of the user.

## Slide 107: Second Generation Systems: Digital TDMA
Concept of Mobile Assisted Hand Off (MAHO)
Mobile station continually measures power levels of surrounding Base Stations and reports these measurements to the serving Base Station.
MAHO method ensures faster hand off MAHO is particularly suited for Micro-Cellular Systems.

## Slide 108: Inter-System Hand Off
Definition: “-----When a mobile moves from one cellular system to another, with different MSC”.
The situation occurs when
“Signal in the resident cell becomes weak, and no other cell within the system can take the call”.
Issues:
Local Call becomes long-distance call
Compatibility between two MSCs.

## Slide 109: Prioritizing the Handoff
Some systems take hand off like a new call initiation
Guard Channel Concept
Reserve some channels exclusively for hand off--- do not use them for call initiation.

## Slide 110: Practical Hand Off Strategies:
High Speed Vehicle VS Pedestrians
Zoning
The UMBRELLA CELL Concept: Large and Small cells are co-located. Install small antennas etc for low-speed users for proper radio coverage. This guarantees large area coverage as well.

## Slide 111: UMBRELLA Cell Approach

## Slide 112: Interference and System Capacity
Creates bottleneck in increasing capacity
Sources of interference are:
Mobile Stations
Neighboring Cells
The same frequency cells
Non-cellular signals in the same spectrum
Interference in Voice Channels: Cross-Talk
Interference in Control Channels: missed/blocked calls

## Slide 113: Interference and System Capacity
In constant cell size and RF power, CCI is a function of Distance between the co-channel cells(D), and the size of each cell (R).
Increasing ratio D/R, CCI decreases.
Define Channel Reuse Ratio = Q = D/R
113
The yellow cells use the same set of
frequency channels, and hence, interfere
with each other
In the cellular system there are 6 first-
layer co-channels

## Slide 114: Interference and System Capacity
Signal-to-interference ratio
S is the power of the signal of interest and is the power of kth interference.
The signal strength at distance d from a source is
That is, received signal power is inversely related to nth power of the distance.
where n = path loss exponent

## Slide 115
Co channel Interference
Mobile Station
Serving Base Station
First tier cochannel Base Station
Second tier cochannel Base Station
R
D1
D2
D3
D4
D5
D6

## Slide 116: Worst Case of CCI

## Slide 118: Cell Splitting

## Slide 119: Cell Sectoring by Antenna Design
119
60o
120o
(a). Omni
(b). 120o sector
(e). 60o sector
120o
(c). 120o sector (alternate)
a
b
c
a
b
c
(d). 90o sector
90o
a
b
c
d
a
b
c
d
e
f

## Slide 120: Cell Sectoring by Antenna Design

## Slide 121: Trunking and Grade of Service (GOS)
Trunking
A means for providing access to users on demand from available pool of channels.
With trunking, a small number of channels can accommodate large number of random users.

## Slide 122: Terminology
Traffic intensity is measured in Erlangs
One Erlang: traffic in a channel completely occupied.
0.5 Erlang: channel occupied 30 minutes in an hour.
Grade of Service (GOS): probability that a call is blocked (or delayed).
Set-Up Time: time to allocate a channel.

## Slide 123: Terminology
Blocked Call: Call that cannot be completed at time of request due to congestion. Also referred to as Lost Call.
Holding Time: (H) average duration of typical call.
Load: Traffic intensity across the whole system.
Request Rate: (λ) average number of call requests per unit time.

## Slide 124: Traffic Measurements

## Slide 125: Traffic Measurements

## Slide 126: Repeaters