## Slide 1: Mobile Communication
Module 6

## Slide 2: Mobile Radio Propagation
Small Scale Multipath Propagation
Impulse Response on a Multipath Channel
Small Scale Path Measurements
Frequency Domain Channel Sounding
Multipath Channel Parameters
Types of Small Scale Fading
Rayleigh & Ricean Distributions
Statistical Models for Multipath Fading Channels

## Slide 3: Mobile Radio Propagation – Small Scale Fading - Multipath
Fading: rapid fluctuations in amplitude over short time & distance
antennas radiate electromagnetic (EM) waves over a wide angle
EM waves reflect off of random objects
transmitted signal arrives at a point from many different paths with different phases
wide variation in phase & amplitude – depending on distribution
large-scale effects are negligible – not distance dependent

## Slide 4: Fading
multipath components (MPCs) – reflected EM wave components
if time delay of MPCs ≈ symbol duration then interference (fading) can result
coherence bandwidth, Bc , is related to channel’s multipath structure
measure of maximum frequency difference between signals with strongly correlated amplitudes
d0
d1
d2
t0 ≈ t1 t2

## Slide 5: Small Scale Multipath Propagation
(i) rapid changes in signal strength over small distances & time intervals
(ii) Doppler shifts on different multipath random frequency modulation
(iii) time dispersion (echoes) caused by multipath

## Slide 6: Multipath in Urban Areas
NLOS path - mobile antenna height < surrounding structure’s height even with LOS path multipath exists
received signal at any point consists of many plane waves with
- randomly distributed amplitudes phases, angles
- components combine vectorially at receiver
- causes distorted or faded signal reception

## Slide 7: Characteristics of Fading
Spatial Fading: all objects are stationary – only mobile moves
spatial variations appear as temporal variations at mobile receiver
constructive & destructive effects of multipath in multipath field
moving objects disturb the field – constructively or destructively

## Slide 8: Characteristics of Fading
High Mobility: receiver passes through several fades in a short time
Low Mobility: extended time in a deep fade possible
Doppler shift: relative mobility between TX & RX proportional to direction & velocity

## Slide 9: Four Factors of Fading
(i) multipath propagation and multipath components (MPCs)
presence of objects cause reflection & scattering
dissipates energy in amplitude, phase, time
multiple versions arrive at different times and spatial orientation
causes signal smearing - intersymbol interference (ISI)

## Slide 10: Four Factors of Fading
(ii) relative speed between Tx-Rx results in Doppler shift – random frequency modulation
(iii) moving objects: induce time varying Doppler shift on MPCs
if speed of objects > mobile speed objects dominates fading
otherwise object speed can be ignored
impact also depends on size & shape of objects

## Slide 11: Four Factors of Fading
(iv)bandwidth of transmitted signal
if signal bandwidth > multipath channel ‘bandwidth’
- received signal will be distorted
- signal strength won’t fade over a small area – insignificant small scale fading
if signal bandwidth << physical channel bandwidth
- rapidly changing signal amplitude - fading
but signal won’t be distorted
signal bandwidth is proportional to 1/symbol duration (width)

## Slide 12
Doppler shift
S = signal source
v = velocity
d = distance Y-X on mobiles path of movement
t = d/v
l = dcos1 = vtcos 1
if S is far away, assume 1 ≈ 2
 =
(4.1)
phase shift:
fd =
(4.2)
Doppler shift = relative frequency change during t
d
Y
X
l
2
1
S
v

## Slide 13
e.g. fc = 1850 MHz   = c/fc = 0.162m
    v = 60mph = 28.62 m/s
    a. mobile moving directly towards transmitter:  = 0o  cos  = 1
    fd = v/ = 160Hz
    f = fc + fd = 1850.00016MHz
  b. mobile moving directly away from transmitter
     = 180o  cos  = -1
  fd = -v/ = -160Hz
    f = fc + fd = 1849.99984MHz
  c. mobile moving  to angle of signal’s arrival
     = 90o  cos  = 0
    fd = 0
S
v
S
v

## Slide 14: Impulse Response on a Multipath Channel
Channel Model used to predict & compare performance of
(i) different communications systems
(ii) different transmission bandwidths for a particular condition
Small Scale Signal Variations are related to RF channels impulse
response
channel impulse response is a wideband channel characterization
contains all information necessary to simulate/analyze any transmission
similar to concept of transfer function and input/ouput in control systems
h(t)
x(t)
y(t)

## Slide 15: (1) Mobile RF Channel Models
i. linear time-invariant (LTI) system
MPCs have variable propagation delays - depending on receiver location
impulse response of LTI channel is a function of receiver position and does not depend on time
ii. linear filter with time-varying impulse response
time variation is due to receiver motion
at time t, many waves are arriving - filter’s nature is result of sum of all amplitudes & delays

## Slide 16
7/23/2019
1.1 Assume time variation is strictly from receiver motion
  v = velocity
  d = fixed position between Tx & Rx
and y(d,t) =
(4.4)
if channel is causal (no output until input is applied) then for t < 0  h(d,t) = 0
let y(d,t) = received signal at position d & time t
  h(d,t) = channel impulse response
  x(t) = transmitted signal
then y(d,t) = x(t)  h(d,t) =
(4.3)
y(d,t)
x(t)
h(t,d)

## Slide 17
1.2 Assume constant v  position at any time t is given by
then y(vt,t) =
(4.6)
y(t)
x(t)
h(vt,t)
since v is constant  received signal y is just a function of t
y(t) =
(4.7)
y(t) = x(t)  h(vt,t) = x(t)  h(d,t)
d = vt (4.5)
channel model: linear time-varying channel that changes with t & d

## Slide 18
1.3 Assume v is constant over short intervals (distances) and let
  x(t) = transmitted bandpass wave form
  y(t) = received waveform
  h(t,) = impulse response of time varying multipath RF channel
    completely characterizes channel
    is a function of variables t & 
      t represents time variation due to motion
       represents channel multipath delay for fixed t
(4.8)
=
y(t) = x(t)  h(t,)
y(t) is the convolution of input signal & channel impulse

## Slide 19
Assume (reasonably) that multipath channel is
  bandlimited
  bandpass
h(t,) is equivalently described by its complex baseband impulse
response hb(t,)
h(t, ) = Re{hb(t, ) exp(jwct) }
h(t, )=Re{hb(t, ) exp(jwct)}
y(t)
x(t)
i. Bandpass Channel Impulse Response Model
x(t) = channel input or transmitted signal
y(t) = channel output or received signal

## Slide 20
½ hb(t, )
r(t)
c(t)
ii. Baseband Equivalent Channel Impulse Response Model
use Complex Envelope to represent transmitted & received signals
r(t) = c(t)  ½ hb(t, )
(4.9)
c(t) & r(t) are complex envelope representations of x(t) & y(t)
x(t) = Re{c(t)exp(j2fct)}
y(t) = Re{r(t)exp(j2fct)}
Complex Envelope properties cause ‘½ ‘ factor in 4.9
  needed to represent passband RF system at baseband
  low pass characterization removes high frequency variations from
  carrier – makes for easier signal analysis

## Slide 21
overbar denotes
  - ensemble average for stochastic signal or
  - time average for deterministic signal
Average Power of band pass signal, x(t) is given by

## Slide 22
i. linear time-invariant (LTI) system
  MPCs have variable propagation delays - depending on receiver
  location
  impulse response of LTI channel is a function of receiver position
  and does not depend on time
ii. linear filter with time-varying impulse response
  time variation is due to receiver motion
  at time t, many waves are arriving - filter’s nature is result of sum
  of all amplitudes & delays
(1) Mobile RF Channel Models
Channel Classification based only on h(t,) , noise is not considered

## Slide 23
1.1 Assume time variation is strictly from receiver motion
  v = velocity
  d = fixed position between Tx & Rx
and y(d,t) =
(4.4)
if channel is causal (no output until input is applied) then for t < 0  h(d,t) = 0
let y(d,t) = received signal at position d & time t
  h(d,t) = channel impulse response
  x(t) = transmitted signal
then y(d,t) = x(t)  h(d,t) =
(4.3)
y(d,t)
x(t)
h(t,d)

## Slide 24
1.2 Assume constant v  position at any time t is given by
then y(vt,t) =
(4.6)
y(t)
x(t)
h(vt,t)
since v is constant  received signal y is just a function of t
y(t) =
(4.7)
y(t) = x(t)  h(vt,t) = x(t)  h(d,t)
d = vt (4.5)
channel model: linear time-varying channel that changes with t & d

## Slide 25
1.3 Assume v is constant over short intervals (distances) and let
  x(t) = transmitted band pass wave form
  y(t) = received waveform
  h(t,) = impulse response of time varying multipath RF channel
    completely characterizes channel
    is a function of variables t & 
      t represents time variation due to motion
       represents channel multipath delay for fixed t
(4.8)
=
y(t) = x(t)  h(t,)
y(t) is the convolution of input signal & channel impulse

## Slide 26
Assume (reasonably) that multipath channel is
  bandlimited
  bandpass
h(t,) is equivalently described by its complex baseband impulse
response hb(t,)
h(t, ) = Re{hb(t, ) exp(jwct) }
h(t, )=Re{hb(t, ) exp(jwct)}
y(t)
x(t)
i. Bandpass Channel Impulse Response Model
x(t) = channel input or transmitted signal
y(t) = channel output or received signal

## Slide 27
(2) Multipath Channels and Delay Spread
  Rx receives a series of replicas of transmitted signal that are attenuated,
  time-delayed, phase-shifted
0
3
2
1
4
each bin has time delay width given by
     = i+1 - i
Let  = multipath delay axis of impulse response
  discretize  into equal time-delay segments or excess delay bins
0
3
2
1
4



## Slide 28
hb(t, )
0 1 2 3 4 5 6 7 8 9
t1
t0
t2
t3
Time-varying Discrete Impulse Response Model for multipath channel
  different snapshots of hb(t, ) at times ti
t0
t1
t2
t3
t

## Slide 29
hb(t, )
(t0)
(t1)
(t2)
t1
t2
t3
t0
t
0 1 2 3 4 … N-2 N-1
(t3)
Time-varying Discrete Impulse Response Model for multipath channel
  time = t varies into the page
  time delay bins are quantized to widths = 
delayed multipath
components
time
amplitude

## Slide 30
hb(t,) =
(4.12)
Baseband Impulse Response of multipath channel:
N = total possible MPCs (bins)
() = unit impulse function – determines specific multipath bins which have
  components at time t & excess delay i
i(t) = excess delay of ith MPC at time t
i(t, ) = real amplitudes of ith MPC at time t
  if i(t,) = 0  excess delay bin has no MPC at time t & delay i
2fci(t)+i(t, ) = all mechanisms for phase shifts of one MPC in ith bin
  includes free-space propagation of ith MPC at time t & any additional
  phase shifts in channel
  often represented as one channel variable: i(t, ) = 2fci(t)+i(t, )

## Slide 31
Assume channel impulse response is either time invariant or stationary over a small time-scale or distance interval
  hb(t,) in (4.12) can be simplified to :
hb(t,) =
(4.13)
i = constant per excess delay bin
i = constant per excess delay bin

## Slide 32
Pass Band Channel Models
r(t) = s(t)  h(t) + n(t)
  r(t) = received signal
  s(t) = transmitted signal
  h(t) = impulse response of channel
  n(t) = AWGN
r(t) =
time invariant channel: i has constant amplitude
if
h() =

r(t) =

## Slide 33: INDOOR AND OUTDOOR PROPAGATION MODELS
What is wireless communication?
  Basically the study of how signals travel in the wireless medium
  To understand wireless networking, we first need to understand the basic characteristics of wireless communications
    How further the signal can travel
    How strong the signal is
    How much reliable would it be (how frequently the signal strength vary)
    Indoor propagation
    Outdoor propagation and
    Many more…
  Wireless communication is significantly different from wired communication

## Slide 34: Wireless Propagation Characteristics
Most wireless radio systems operate in urban area
  No direct line-of-sight (los) between transmitter and receiver
Radio wave propagation attributed to
  Reflection
  Diffraction and
  Scattering
Waves travel along different paths of varying lengths
  Multipath propagation
  Interaction of these waves can be constructive or destructive
Reflection (R), diffraction (D) and scattering (S).

## Slide 35: Wireless Propagation Characteristics(contd.)
Strengths of the waves decrease as the distance between Tx and Rx increase
We need Propagation models that predict the signal strength at Rx from a Tx
One of the challenging tasks due to randomness and unpredictability in the surrounding environment
Pr
Pt
d=vt
v

## Slide 36: Wireless Propagation Models
Can be categorized into two types:
  Large-scale propagation models
  Small-scale propagation models
Large-scale propagation models
  Propagation models that characterize signal strengths over Tx-Rx separation distance
Small-scale propagation models
  Characterize received signal strengths varying over short scale
    Short travel distance of the receiver
    Short time duration

## Slide 37: Wireless Propagation Models (contd.)
Large-scale propagation
Small-scale propagation
Pr
Pt
d=vt
v
Pr/Pt
d=vt
Very slow
Fast

## Slide 38: Large-scale propagation model
Also known as Path loss model
There are numerous path loss models
  Free space path loss model
    Simple and good for analysis
    Mostly used for direct line-of-sight
    Not so perfect for non-LOS but can be approximated
  Ray-tracing model
    2-ray propagation model
    Site/terrain specific and can not be generalized easily
  Empirical models
    Modeled over data gathered from experiments
    Extremely specific
    But more accurate in the specific environment

## Slide 39: Free space Path Loss Model
What is the general principle?
  The received power decays as a function of Tx-Rx separation distance raised to some power
  i.e., power-law function
Path loss for unobstructed LOS path
Power falls off :
  Proportional to d2

## Slide 40: Free space Path Loss Model (contd.)

## Slide 41: Free space Path Loss (contd.)
What is the path loss?
  Represents signal attenuation
  What will be the order of path loss for a FM radio system that transmits with 100 kW with 50 km range?
  Also calculate: what will be the order of path loss for a Wi-Fi radio system that transmits with 0.1 W with 100 m range?

## Slide 42: Path Loss in dB
It is difficult to express Path loss using transmit/receive power
  Can be very large or
  Very small
Expressed as a positive quantity measured in dB
  dB is a unit expressed using logarithmic scale
  Widely used in wireless
  With unity antenna gain,

## Slide 43: dBm and dBW
dBm and dBW are other two variations of dB
  dB references two powers (Tx and Rx)
  dBm expresses measured power referenced to one mW
    Particularly applicable for very low received signal strength
  dBW expresses measured power referenced to one watt
  dBm Widely used in wireless
  P in mW

## Slide 44: Path Loss model
We saw Path loss expressed in dB
  Note, the above eqn does not hold for d=0
For this purpose, a close-in distance d0 is used as a reference point
  It is assumed that the received signal strength at d0 is known
  Received signal strength is then calculated relative to d0
  For a typical Wi-Fi analysis, d0 can be 1 m.

## Slide 45: Indoor Propagation Model
The indoor radio channel differs from the traditional mobile radio channel in outdoor
  Distances covered are much smaller
  Variability of the environment is much greater
Propagation inside buildings strongly influenced by specific features
  Layout and building type
  Construction materials
  Even door open or closed
  Same floor or different floors
Partition Losses

## Slide 46: Partition Loss
Partition Losses
  Same floor
  Between floors
    Characterized by a new factor called Floor Attenuation Factors (FAF)
    Based on building materials
    FAF mostly empirical (computed over numerous tests)
  For example,
    FAF through one floor approx. 13 dB
    Two floors 18.7 dB
    Three floors 25 dB and so on…

## Slide 47: Cellular Model (signal to interference)
From the propagation model,
Let’s combine today’s concept with last week’s cellular concept
  Let’s find out signal to interference
m co-channel
interferer
Cell radius R
Co-channel
interferer distance Di
Q: co-channel
Reuse ratio

## Slide 48: Knife-edge Diffraction Model
Estimating the signal attenuation caused by diffraction of radio waves over hills and buildings is essential in predicting the field strength in a given service area.
Generally, it is impossible to make very precise estimates of the diffraction losses, and in practice prediction is a process of theoretical approximation modified by necessary empirical corrections.
Though the calculation of diffraction losses over complex and irregular terrain is a mathematically difficult problem, expressions for diffraction losses for many simple cases have been derived.
As a starting point, the limiting case of propagation over a knife-edge gives good insight into the order of magnitude of diffraction loss.

## Slide 49: Knife-edge Diffraction Model
When shadowing is caused by a single object such as a hill or mountain, the attenuation caused by diffraction can be estimated by treating the obstruction as a diffracting knife edge.
This is the simplest of diffraction models, and the diffraction loss in this case can be readily estimated using the classical Fresnel solution for the field behind a knife edge (also called a half-plane). Figure illustrates this approach.
Consider a receiver at point R, located in the shadowed region (also called the diffraction zone).

## Slide 50: Knife-edge Diffraction Model
The field strength at point R in Figure is a vector sum of the fields due to all of the secondary Huygens sources in the plane above the knife edge.
The diffraction gain due to the presence of a knife edge, as compared to the free space E-field, is given by
Gd(dB) = 2OlogIF(v)!

## Slide 52: Knife-edge Diffraction Model

## Slide 53: Rayleigh and Ricean Distributions
Rayleigh Fading Distribution
In mobile radio channels, the Rayleigh distribution is commonly used to describe the statistical time varying nature of the received envelope of a flat fading signal, or the envelope of an individual multipath component.
It is well known that the envelope of the sum of two quadrature Gaussian noise signals obeys a Rayleigh distribution.
Figure shows a Rayleigh distributed signal envelope as a function of time. The Rayleigh distribution has a probability density function (pdf) given by
where alpha is the rms value of the received voltage signal before envelope detection,
and alpha is the time-average power of the received signal before envelope detection.

## Slide 54: Rayleigh distribution

## Slide 55: Rayleigh distribution
Thus the mean and the median differ by only 0.55 dB in a Rayleigh fading signal.
Note that the median is often used in practice, since fading data are usually measured in the field and a particular distribution cannot be assumed

## Slide 56: Rician Distribution
When there is a dominant stationary (nonfading) signal component present, such as a line-of-sight propagation path, the small-scale fading envelope distribution is Ricean.
In such a situation, random multipath components arriving at different angles are superimposed on a stationary dominant signal.
At the output of an envelope detector, this has the effect of adding a dc component to the random multipath.

## Slide 57: Rician Distribution
The parameter K is known as the Ricean factor and completely specifies the Ricean distribution. As A —*0, K —* dB, and as the dominant path decreases in amplitude, the Ricean distribution degenerates to a Rayleigh distribution.